## Slide 1
Waveform Tuning Models
Finding optimal printer settings with machine learning
Canon Production Printing · 4 Predictive Models · Random Forest
1 / 8

## Slide 2
The Problem
30 chips × 1,120 nozzles
Each nozzle must fire consistently. V, F_r, dt2 control ink output. Testing every combination is slow and expensive.
Our approach
Train ML models on existing experiment data. Predict print quality for untested settings. Rank candidates — run only the best ones physically.
Tunable inputs: V (voltage) · F_r (flow rate) · dt2 (timing)
Context (fixed by print job): Color$ · Coverage#
2 / 8

## Slide 3
Why Four Models?
Two questions × two scales
What SD level?
How consistent?
Within one chip
Across all 30 chips
Model 3
sd_mean Avg nozzle density per chip
Model 1
sd_std Nozzle spread within chip
Model 4
cross_chip_mean Avg density across 30 chips
Model 2
cross_chip_std Chip consistency across printhead
★ Model 2 + Model 4 together give the most complete answer for Canon
3 / 8

## Slide 4
Model Performance
Model
Target
Algorithm
R²
Test Strategy
Model 1
sd_std
Random Forest
0.845
Chips 25–30 held out ✓
Model 2
cross_chip_std
Random Forest
0.998 *
Random 80/20
Model 3
sd_mean
Random Forest
0.995
Chips 25–30 held out ✓
Model 4
cross_chip_mean
Random Forest
0.998 *
Random 80/20
* Random 80/20 split from the same experiment — likely overestimates real-world performance
Random Forest outperformed XGBoost and Linear Regression across all four models
4 / 8

## Slide 5
What Drives Print Variability?
Feature importance from Model 1 (Random Forest)
Color$
31%
Coverage#
27%
V × F_r
14%
V
10%
F_r
8%
dt2 × Cov
5%
V²
3%
F_r²
2%
Color and Coverage are the dominant drivers — but they cannot be tuned. V, F_r, dt2 are the levers Canon actually controls.
5 / 8

## Slide 6
Finding the Best Settings
Cell 9 — Target SD Search (example: Color = C, Coverage = 22, target SD = 0.35)
target_sd = 0.35 tolerance = 0.02 color = 'C' coverage = 22.0
→
V
F_r
dt2
cross_chip_mean
cross_chip_std
20.0
1.14
-900
0.349
0.0021
21.0
1.10
-900
0.352
0.0023
20.0
1.10
-700
0.351
0.0028
↑ lowest cross_chip_std = most consistent across all 30 chips
The model filters candidates to those hitting the target density, then ranks them by cross-chip consistency — giving a direct actionable recommendation.
6 / 8

## Slide 7
Interactive Dashboard
Measured Tab
Direct lookup from real experiment data. No model involved — fully reliable. Shows all tested settings for the selected color and coverage.
Predicted Tab
Uses the Random Forest model. Predicts for untested V × F_r × dt2 combinations. Marks each row as tested: yes / no.
Optional: set a target SD → results are filtered to settings that achieve that density
streamlit run app.py
7 / 8

## Slide 8
Limitations & Next Steps
Current Limitations
– R²=0.998 for Models 2 & 4 comes from a random split of the same experiment — not tested on new hardware
– All models trained on one print run with 30 chips from one batch — generalisation unknown
– Random Forest interpolates but cannot extrapolate beyond the range of training values
– No input validation in the dashboard — out-of-range inputs produce unreliable predictions
Next Steps
1. Validate on a second independent print run
2. Add input validation — reject out-of-range values
3. Wrap model as an API for Canon's systems
4. Test on different printhead hardware batch
Current state: working proof of concept — the recommended settings table is already useful to Canon
8 / 8